Building ID:       		Date:       		Name of Evaluator(s):

Building Contact:  Name:       		Phone:       		Email:

Building Name & Address:

Subdivision:       		Lot #:       		Conditioned Floor Area:       	ft2

State:       		County:       		Jurisdiction:

Compliance Approach (check all that apply):    Prescriptive     Trade-Off     Performance

Compliance Software Used:       		Green Building/Above-Code Program:

Building Type:  		1- and 2-Family, Detached:	 Single Family	 Modular	 Townhouse

Multifamily:	 Apartment	 Condominium

Project Type:	 New Building	 Existing Building Addition	 Existing Building Renovation

| IECC Section # | Pre-Inspection/Plan Review | Code Value | Verified Value | Complies | Comments/Assumptions |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Y | N | N/A |  |
| 103.2 [PR1]1 | Construction drawings and documentation available. Documentation sufficiently demonstrates energy code compliance. |  |  |  |  |  |  |
| 403.6 [PR2]2 | HVAC loads calculations: Heating system size(s): Cooling system size(s): |  | kBtu: kBtu: |  |  |  |  |

# Additional Comments/Assumptions:

General building information only required if different than above 	Building ID:

Date:       		Name of Evaluator(s):

Building Name & Address:       		Conditioned Floor Area:         	ft2

Building Contact:  Name:       		Phone:       		Email:

Compliance Approach (check all that apply):    Prescriptive     Trade-Off     Performance

Compliance Software Used:       		Green Building/Above-Code Program:

| IECC Section # | Foundation Inspection | Code Value | Verified Value | Complies | Comments/Assumptions |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Y | N | N/A |  |
| 402.1.1 [FO1]1 | Slab edge insulation R-value. | Unheated: R-10 Heated: R-15 | R- Unheated Heated |  |  |  |  |
| 303.2, 402.2.8 [FO2]1 | Slab edge insulation Installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 402.1.1 [FO3]1 | Slab edge insulation depth/length. | 4 ft. | ft. |  |  |  |  |
| 402.1.1 [FO4]1 | Basement wall exterior insulation R-value. | Continuous: R-15 | R- |  |  |  |  |
| 303.2 [FO5]1 | Basement wall exterior insulation installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 402.2.7 [FO6]1 | Basement wall exterior insulation depth. | 10 ft. or to basement floor | ft. |  |  |  |  |
| 402.2.9 [FO7]1 | Crawl space wall insulation R-value. | Continuous: R-10 Cavity: R-13 | R- R- |  |  |  |  |
| 303.2 [FO8]1 | Crawl space wall insulation installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 402.2.9 [FO9]1 | Crawl space continuous vapor retarder installed with joints overlapped by 6 inches and sealed, and extending at least 6” up the stem wall. |  |  |  |  |  |  |
| 303.2.1 [FO10]2 | Exposed foundation insulation protection. |  |  |  |  |  |  |
| 403.8 [FO11]2 | Snow melt controls. |  |  |  |  |  |  |

# Additional Comments/Assumptions:

General building information only required if different than above 	Building ID:

Date:       		Name of Evaluator(s):

Building Name & Address:       		Conditioned Floor Area:         	ft2

Building Contact:  Name:       		Phone:       		Email:

Compliance Approach (check all that apply):    Prescriptive     Trade-Off     Performance

Compliance Software Used:       		Green Building/Above-Code Program:

| IECC Section # | Framing / Rough-In Inspection | Code Value | Verified Value | Complies | Comments/Assumptions |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Y | N | N/A |  |
| 402.1.1, 402.3.4 [FR1]1 | Door U-factor. | U-0.35 | U- |  |  |  |  |
| 402.1.1, 402.3.3, 402.5 [FR2]1 | Glazing U-factor (area-weighted average). | U-0.35 (0.4 max) | U- |  |  |  |  |
| 402.1.1, 402.3.3 [FR3]1 | Glazing SHGC value, including sunrooms (area-weighted average). 4 | N/A | SHGC: |  |  |  |  |
| 303.1.3 [FR4]1 | Glazing labeled for U-factor (or default values used). |  |  |  |  |  |  |
| 402.1.1, 402.3.3, 402.5 [FR5]1 | Skylight U-factor. 4 | U-0.6 (0.75 max)5 | U- |  |  |  |  |
| 402.1.1, 402.3.3 [FR6]1 | Skylight SHGC value.4 | N/A | SHGC: |  |  |  |  |
| 303.1.3 [FR7]1 | Skylights labeled for U-factor (or default values used). |  |  |  |  |  |  |
| 402.3.5 [FR8]1 | Sunroom glazing U-factor. | U-0.5 | U- |  |  |  |  |
| 402.3.5 [FR9]1 | Sunroom skylight U-factor. | U-0.75 | U- |  |  |  |  |
| 402.1.1 [FR10]1 | Mass wall exterior insulation R-value. | R-15 | R- |  |  |  |  |
| 303.2 [FR11]1 | Mass wall exterior insulation installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 403.2.1 [FR12]1 | Duct insulation. | Attic Supply: R-8 Other: R-6 | R- R- |  |  |  |  |
| 403.2.2 [FR13]1 | Duct sealing complies with listed sealing methods. |  |  |  |  |  |  |
| 403.2.2 [FR14]1 | Duct tightness via rough-in test. If applicable, verification via post-construction test should be marked N/A. | Across System: 6 cfm No Air Handler:: 4 cfm | cfm |  |  |  |  |
| 403.2.3 [FR15]1 | Building cavities NOT used for supply ducts. |  |  |  |  |  |  |
| 402.4.5 [FR16]2 | IC-rated recessed lighting fixtures meet infiltration criteria. |  |  |  |  |  |  |
| 403.3 [FR17]2 | HVAC piping insulation. | R-3 | R- |  |  |  |  |
| 403.4 [FR18]2 | Circulating hot-water piping insulation. | R-2 | R- |  |  |  |  |
| 403.5 [FR19]2 | Dampers Installed on all outdoor Intake and exhaust openings. |  |  |  |  |  |  |
| 402.4.4 [FR20]3 | Glazed fenestration air leakage. | 0.3 cfm/ft2 | cfm/ ft2 |  |  |  |  |
| 402.4.4 [FR21]3 | Swinging door air leakage. | 0.5 cfm/ft2 | cfm/ ft2 |  |  |  |  |
| 402.4.4 [FR22]3 | Fenestration and doors labeled for air leakage. |  |  |  |  |  |  |

# Additional Comments/Assumptions:

General building information only required if different than above 	Building ID:

Date:       		Name of Evaluator(s):

Building Name & Address:       		Conditioned Floor Area:       	ft2

Building Contact:  Name:       		Phone:       		Email:

Compliance Approach (check all that apply):    Prescriptive     Trade-Off     Performance

Compliance Software Used:       		Green Building/Above-Code Program:

| IECC Section # | Insulation Inspection | Code Value | Verified Value | Complies | Comments/Assumptions |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Y | N | N/A |  |
| 402.1.1, 402.2.5, 402.2.6 [IN1]1 | Floor insulation R-value. | Wood: R-30 Steel: See footnote | R- Wood Steel |  |  |  |  |
| 303.2 [IN2]1 | Floor insulation installed per manufacturer’s instructions, and in substantial contact with the subfloor. |  |  |  |  |  |  |
| 402.1.1 402.2.5 402.2.4 [IN3]1 | Wall insulation R-value. | Wood: R-20 or R-13+R-5 Mass: R-19 Steel: See footnote | R- Wood Mass Steel |  |  |  |  |
| 303.2 [IN4]1 | Wall insulation installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 402.1.1 [IN5]1 | Basement wall interior insulation R-value. | Continuous: R-15 Cavity: R-19 | R- R- |  |  |  |  |
| 303.2 [IN6]1 | Basement wall interior insulation installed per manufacturer’s Instructions. |  |  |  |  |  |  |
| 402.2.7 [IN7]1 | Basement wall interior insulation depth. | 10 ft or to basement floor | ft |  |  |  |  |
| 402.2.11 [IN8]1 | Sunroom wall insulation R-value. | R-13 | R- |  |  |  |  |
| 303.2 [IN9]1 | Sunroom wall insulation installed per manufacturer’s Instructions. |  |  |  |  |  |  |
| 402.2.11 [IN10]1 | Sunroom ceiling insulation R-value. | R-24 | R- |  |  |  |  |
| 303.2 [IN11]1 | Sunroom ceiling insulation installed per manufacturer’s instructions. |  |  |  |  |  |  |
| 402.4.2, 402.4.2.1 [IN12]1 | Air sealing complies with sealing requirements via blower door test. If applicable, verification via visual inspection should be marked N/A. | ACH 50 ≤ 7 | ACH 50 = |  |  |  |  |
| 303.1 [IN13]2 | All installed insulation labeled or installed R-value provided. |  |  |  |  |  |  |
| 402.4.1, 402.4.2 [IN14]3 | Air sealing of all openings and penetrations via visual inspection: Site-built fenestration Window/door openings Utility penetrations Attic access openings If applicable, verification via blower door should be marked N/A. |  |  |  |  |  |  |
| 402.4.1, 402.4.2 [IN15]3 | Air sealing of all envelope joints and seams via visual inspection: Dropped ceilings Knee walls Assemblies separating garage Tubs and showers Common walls between units Rim joist junctions If applicable, verification via blower door should be marked N/A. |  |  |  |  |  |  |
| 402.4.1, 402.4.2 [IN16]3 | Air sealing of all other sources of infiltration, including air barrier, via visual inspection. If applicable, verification via blower door should be marked N/A. |  |  |  |  |  |  |

# Additional Comments/Assumptions:

General building information only required if different than above 	Building ID:

Date:       		Name of Evaluator(s):

Building Name & Address:       		Conditioned Floor Area:         	ft2

Building Contact:  Name:       		Phone:       		Email:

Compliance Approach (check all that apply):    Prescriptive     Trade-Off     Performance

Compliance Software Used:       		Green Building/Above-Code Program:

| IECC Section # | Final Inspection Provisions | Code Value | Verified Value | Complied | Comments/Assumptions |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Y | N | N/A |  |
| 402.1.1 402.2.1 402.2.2 [FI1]1 | Ceiling insulation R-value. | Wood: R-49 Steel Truss: R-38+R-5 Steel Joist: R-49 | R- Wood Steel |  |  |  |  |
| 303.1.1.1, 303.2 [FI2]1 | Ceiling insulation installed per manufacturer’s instructions. Blown insulation marked every 300 ft2. |  |  |  |  |  |  |
| 402.2.3 [FI3]1 | Attic access hatch and door insulation. | R-49 | R- |  |  |  |  |
| 403.2.2 [FI4]1 | Duct tightness via post-construction test. If applicable, verification via rough-in test should be marked N/A. | To Outdoors: 8 cfm Across System: 12 cfm | cfm |  |  |  |  |
| 403.6 [FI5]1 | Heating and cooling equipment type and capacity as per plans. |  |  |  |  |  |  |
| 404.1 [FI6]1 | Lighting - 50% of lamps are high efficacy. |  |  |  |  |  |  |
| 401.3 [FI7]2 | Certificate posted. |  |  |  |  |  |  |
| 402.4.3 [FI8]2 | Wood burning fireplace - gasketed doors and outdoor air for combustion. |  |  |  |  |  |  |
| 403.1.1 [FI9]2 | Programmable thermostats installed on forced air furnaces. |  |  |  |  |  |  |
| 403..1.2 [FI10]2 | Heat pump thermostat installed on heat pumps. |  |  |  |  |  |  |
| 403.4 [FI11]2 | Circulating service hot water systems have automatic or accessible manual controls. |  |  |  |  |  |  |
| 403.9 [FI12]2 | Pool heaters, covers, and automatic or accessible manual controls. |  |  |  |  |  |  |

# Additional Comments/Assumptions:

| KEY | 1 | High Impact (Tier 1) | 2 | Medium Impact (Tier 2) | 3 | Low Impact (Tier 3) |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

# Footnotes

Use Comments/Assumptions to document code requirements that pass due to exceptions, and specify the exception. Also use Comments/Assumptions to document multiple values observed for a given code requirement, such as multiple equipment efficiencies.

Basement insulation is not required in warm-humid locations.

One side-hinged door up to 24 ft2 can be exempted from the prescriptive door U-factor requirements.

Up to 15 ft2 of glazed fenestration, including skylights, may be exempted from U-factor and SHGC requirements under the prescriptive approach.

U-factor mandatory maximum using trade-offs.

If more than ½ the insulation is on the interior, mass wall interior insulation requirement applies (R-19).

Or insulation sufficient to fill the cavity, R-19 minimum.

Floor steel frame equivalent: R-19+R-6 in 2x6 or R-19+R-12 in 2x8 or 2x10

If more than ½ the insulation is on the exterior, mass wall exterior insulation requirement applies (R-15).

Wall steel frame equivalent: R-13+R-10; R-19+R-9; R-25+R-8.

R-38 if insulation is not compressed at eaves. R-30 may be used for 500 ft2 or 20% (whichever is less) where sufficient space is not available.